## Slide 1: Access to Opportunity

## Slide 2: Learning Objectives
Analyze the complex relationship between the built environment and accessibility
Describe how the economic and social mobility of various population groups are affected by transportation.
Apply strategies and tools to increase the access to employment, education, affordable housing, and transportation for underserved communities

## Slide 3: Accessibility and the Built Environment

## Slide 4: Mobility and Accessibility
Mobility
The ability of people to make trips to satisfy their needs or desires by any combination of modes of transportation.
An area-wide measure of the ease of travel between locations within a defined geographic area.
Accessibility
Notes: Key Message: Accessibility and mobility are key to equitable transportation systems
Taking Points:
Mobility measures people’s ability to make trips to satisfy their needs or desires using any combination of transportation modes.
Accessibility measures how easily people can travel between locations within a defined geographic area
Places that are highly accessible can be reached by many people quickly, whereas inaccessible places can only be reached by a few people in the same amount of time.

## Slide 5: Accessibility versus Mobility Video
https://www.youtube.com/watch?v=4OMv6CqrzvE
Notes: Video of Susan Handy discussing the different relationships between accessibility and mobility
(5 minutes 14 seconds)
https://www.youtube.com/watch?v=4OMv6CqrzvE

## Slide 6: Accessibility
Accessibility
Land Use
Transportation Network
Opportunities
  Number
  Variety
  Proximity
Travel Time
  Connectivity
  Directness
  Safety
Notes: Key message: It is important to improve accessibility, as well as mobility, and to think about both terms broadly in terms of moving people rather than just vehicles and organizing land uses so they are more accessible via a variety of modes and paths. Access to education, jobs, affordable shopping and healthcare facilitated through multimodal transportation (integrated transportation and land use) is particularly important for physically, economically and socially disadvantaged groups who are vulnerable users of the transportation system
Talking Points:
Destination accessibility is often used as a measure to reduce vehicle miles traveled (VMT), but poor accessibility results in high VMT as a consequence of sprawl.
To provide a highly accessible setting, where an individual will have access to a wide array of goods and services, employment as well as social opportunities (the more density the more opportunities) and a transportation system that connects them to those opportunities with a variety of mode choices and service options (bike share, car share, zip car, etc.)
Suggestion:
Before you move to the next slide, complete the knowledge probe activity Module 6 Probe Question #1 (see the module outline for more information):
In what ways does accessibility specifically affect underserved communities? Consider both the short-term and long-term impacts on individuals and on the community (including socio-economic mobility). Explain the thought process behind your answers.
Throughout the lecture, encourage them to think about strategies that can increase equitable access to opportunity. At the end of the lecture, ask students to discuss the strategies they identified, including any potential consequences of these strategies and necessary mitigating measures.
References:
Litman, T. (2021). Evaluating Transportation Equity. https://vtpi.org/equity.pdf
Williams, K., and Seggerman, K. (2014). Multimodal Transportation Best Practices and Model Element. https://www.nctr.usf.edu/wp-content/uploads/2015/08/77954.pdf

## Slide 7: Achieving More Equitable Access to Opportunity
Multimodal transportation can provide better access to opportunity and improve mobility options for underserved populations.
Source: https://files.wri.org/s3fs-public/from-mobility-to-access-for-all.pdf
Notes: Key Message: The figure shows how access-based approaches through multimodal transportation can provide better access to opportunities and better mobility options and reduce mobility costs for underserved populations.
Talking Points:
There are a few ways that we can measure access to opportunity. Two common measurements include:
The number of potential opportunities (destinations) that can be reached within a certain amount of time.
The cost to move between origin and destination, and opportunities available at the destination.
References:
Venter, C., Mahendra, A., & Hidaslo, D. (2019). From Mobility to Access for All: Expanding Urban Transportation Choices in the Global South [Working Paper]. https://files.wri.org/s3fs-public/from-mobility-to-access-for-all.pdf

## Slide 8: Transportation Affordability

## Slide 9: Transportation Affordability
A measure of a household’s ability to afford transportation
Low-income households are disproportionately burdened by transportation costs
Source: https://www.pewtrusts.org/~/media/assets/2016/03/household_expenditures_and_income.pdf
Notes: Key Message: Housing and transportation are the two largest household expenditures. Lower-income families spend a larger share of income on transportation than middle- and high-income families
Talking Points:
Transportation costs are estimated based on land use mix, commute patterns, and socioeconomic information
Affordability is most effectively measured by combining transportation and housing costs
References:
VTPI. (2016) Transportation affordability. https://www.vtpi.org/tdm/tdm106.htm
Litman, T. (2021). Transportation affordability: Evaluation and improvement strategies. https://www.vtpi.org/affordability.pdf
US DOT. (2015) Housing and transportation affordability. https://www.transportation.gov/mission/health/housing-and-transportation-affordability
Pew Charitable Trusts. (2016). Household expenditures and income. https://www.pewtrusts.org/~/media/assets/2016/03/household_expenditures_and_income.pdf
Litman, T. (2013). Affordability as a transportation planning objective. https://www.planetizen.com/node/60908
Jaffe, E. (2013). 3 charts that explain why you spend so much on transportation. https://www.bloomberg.com/news/articles/2013-03-04/3-charts-that-explain-why-you-spend-so-much-on-transportation

## Slide 10: Tool: Center for Neighborhood Technology H+T Index
Access the index here: https://www.cnt.org/tools/housing-and-transportation-affordability-index
Provides an understanding of affordability
Includes housing and transportation costs
Notes: Key Message: The Housing and Transportation Affordability Indicator measures the percent of household income spent on housing and transportation
References:
CNT. (n.d.) Housing + transportation index. https://www.cnt.org/tools/housing-and-transportation-affordability-index

## Slide 11: Affordability Example: H+T Index
Association of Bay Area Governments
Evaluated regional planning scenarios using H+T Index as % of income
Source: MTC and ABAG, 2013
Notes: Talking Points:
Association of Bay Area Government’s (serves as MPO for San Francisco metro area)
Used a housing and transportation cost index in their 2013 regional plan to evaluate the equity impacts of various plan scenarios on communities of concern. The metric compares affordability between lower income individuals (those making under $38,000 a year) and those of higher income on a regional basis.
Average housing costs per household are combined with transportation costs and divided by average income.
References:
Association of Bay Area Governments and Metropolitan Transportation Commission. (2013). Equity analysis report: Including Title VI, environmental justice and equity analysis for plan bay area. https://www.planbayarea.org/sites/default/files/pdf/final_supplemental_reports/FINAL_PBA_Equity_Analysis_Report.pdf

## Slide 12: City of Tampa, Florida Case Example
Source: https://www.cutr.usf.edu/wp-content/uploads/2021/09/The-Transportation-Equity-Scorecard-User-Guide.pdf
Concentration of Underserved Populations
Project Information
Notes: Key Message: The maps show and example of housing affordability and the transportation cost index in underserved communities in relation to a proposed project
Suggestion:
Before you move to the next slide, complete the knowledge probe activity Module 6 Probe Question #2 (see the module outline for more information):
What strategies can agencies use to reduce transportation and housing costs for underserved communities?
References:
Williams, K. et al. (2020). Transportation equity scorecard – A tool for project screening and prioritization. https://www.cutr.usf.edu/wp-content/uploads/2021/09/The-Transportation-Equity-Scorecard-User-Guide.pdf

## Slide 13: Affordability Questions to Consider
What is the share of household income consumed by transportation and housing?
What strategies can be used to reduce housing and transportation costs as a percent of income to 30 percent or less?
What strategies can reduce travel time or eliminate a barrier to/from affordable housing?
Are there opportunities for direct connections to affordable housing through premium transit service, a protected bicycle facility, or new/connected sidewalks or shared use paths?
Are there opportunities to significantly decrease travel time to and from affordable housing?
Is there access to affordable transportation choices, especially in areas with a high transportation cost?
Is there premium and affordable transit or protected and connected bike facility or new/connected sidewalk or increase the availability of high quality and affordable transportation options?
Notes: Suggestion:
Before you move to the next slide, complete the knowledge probe activity Module 6 Probe Question #3 (see the module outline for more information):
What pertinent questions might transportation professional ask when assessing transportation affordability in a community?
What sources might agency staff use to better understand affordability in a community?

## Slide 14: Spatial Mismatch

## Slide 15: What is Spatial Mismatch?
Gap between where low-income workers live and where job opportunities are located.
Notes: Key Message: There is a gap between where jobs are and where people live that disproportionately affects underserved communities including hourly, low entry barrier, and shift jobs
Talking Points:
Spatial mismatch is influenced by:
  Transportation accessibility and affordability
  Land use and development
It results in:
  High unemployment rates
  Extensive spells of joblessness
Spatial mismatch most significantly affects:
  Low-income households
  Zero vehicle households
  Households with limited or no access to transit
  Minority communities
References:
Dowell, E. (2020). Job sprawl results in unemployment for low-income urban residents. https://www.census.gov/library/stories/2020/03/spatial-mismatch-when-workers-can-not-get-to-jobs-in-suburbs.html
Stacy, C. et al. (2019). Too far from jobs: spatial mismatch and hourly workers. https://www.urban.org/features/too-far-jobs-spatial-mismatch-and-hourly-workers

## Slide 16: Job Growth and Spatial Mismatch between Jobs and Low-Income Residents
https://www.census.gov/data/academy/webinars/2019/job-growth-spatial-mismatch.html
Notes: Webinar by Reza Sardari, PH.D., GISP discussing job sprawl and its impact on access to opportunity for low-income families in the Dallas Fort Worth region
(50 minutes 22 seconds)
https://www.census.gov/data/academy/webinars/2019/job-growth-spatial-mismatch.html
*The link provides access to the webinar recording, presentation, and transcript

## Slide 17: Calculating Spatial Mismatch
Uses GIS and other mapping software
  Draw a buffer around the population-weighted centroid (the mean center of the population).
  Subtract all job seekers in the buffer from the job postings in the buffer.
  Evaluate results:
    Larger numbers = greater employer spatial mismatch
    Smaller numbers = greater job seeker spatial mismatch
Source: https://www.census.gov/library/stories/2020/03/spatial-mismatch-when-workers-can-not-get-to-jobs-in-suburbs.html
Notes: Key Message: Spatial mismatch is calculated using mapping software to visualize where job seekers live and where employment is located
Talking points:
Stacy et al. (2019) explain that when analyzing the effects of spatial mismatch on hourly workers, “We calculate the population-weighted centroid for each zip code by taking population counts from the American Community Survey at the census block group level and geospatially calculating the mean center of each zip code weighted by the distribution of population by census block group.”
References:
Stacy, C. et al. (2019). Too far from jobs: spatial mismatch and hourly workers. https://www.urban.org/features/too-far-jobs-spatial-mismatch-and-hourly-workers

## Slide 18: San Francisco Case Example
Source: https://www.urban.org/features/too-far-jobs-spatial-mismatch-and-hourly-workers
In this example “reasonable distance” is defined as 6.3 miles.
6.3 miles is the average distance between each job seeker and job posting for all applicants in the dataset.
Notes: Key Message: The map shows the locations of jobs posted and the location of job applicants within a reasonable distance of each zip code in the San Francisco Bay Area.
References:
Stacy, C. et al. (2019). Too far from jobs: spatial mismatch and hourly workers. https://www.urban.org/features/too-far-jobs-spatial-mismatch-and-hourly-workers

## Slide 19: Opportunity Mapping
Used to visualize:
  Levels of opportunity (very low to very high)
  Communities that are underinvested
Indicators:
  Education
  Economic health
  Housing and neighborhood quality
  Mobility and Transportation
  Health and Environment
The goal is to guide investment in areas of low opportunity and create connections to high-opportunity neighborhoods.
Notes: Key Message: “Areas of opportunity that experience greater proportions of growth may experience an increased risk of displacement.” Puget Sound Regional Council (n.d.)
Talking points:
Social and economic mobility relate to access to opportunity.
Economic mobility is the ability to change an individual’s, family’s, or groups’ economic status (i.e. moving income brackets, acquiring or increasing wealth)
Social mobility is the ability to move from one social position to another (can include income and wealth, but also includes occupation, political power, etc.)
Suggestion:
Before you move to the next slide, complete the knowledge probe activity Module 6 Probe Question #4 (see the module outline for more information):
In what ways does transportation affect opportunities for social and economic mobility?
References:
Chetty, R., and Hendren, N. (2017). The impacts of neighborhoods on intergenerational mobility I: Childhood exposure effects. https://opportunityinsights.org/wp-content/uploads/2018/03/movers_paper1.pdf
Kirwan Institute for the Study of Race and Ethnicity. (2012). Equity, opportunity, and sustainability in the Central Puget Sound Region: Geography of opportunity in the Central Puget Sound. Regionhttp://www.kirwaninstitute.osu.edu/reports/2012/05_2012_PugetSoundOppMapping.pdf
Puget Sound Regional Council. (n.d.) Opportunity mapping report. https://psregcncl.maps.arcgis.com/apps/MapSeries/index.html?appid=6ecc0239067e4c00809e0d6bcdee4e64
U.S. Department of Housing and Urban Development's (HUD's) Office of Policy Development and Research (PD&R). (2015). Moving toward a sustainable future: Three models of regional planning.
https://www.huduser.gov/portal/periodicals/em/fall15/highlight3.html

## Slide 20: Puget Sound Case Example
Source: https://psregcncl.maps.arcgis.com/apps/webappviewer/index.html?id=04178e4d496d4cd0ae87bb5182bdc94d
“Census tracts that are considered “high” or “very high” opportunity areas have relatively more resources than the regional average, while those that are considered “low” or “very low” have relatively fewer resources.”
-Puget Sound Regional Council
Notes: Key Message: The map shows the comprehensive opportunity map for a section of the Puget Sound region
Talking points:
The Puget Sound example demonstrates a method for assessing access to opportunity that uses indicators to determine areas of different levels of opportunity with a goal to" guide investment in areas of low opportunity and strengthen connections to high-opportunity neighborhoods“
References:
Puget Sound Regional Council. (n.d.) Opportunity mapping report. https://psregcncl.maps.arcgis.com/apps/MapSeries/index.html?appid=6ecc0239067e4c00809e0d6bcdee4e64

## Slide 21: Strategies to Address Spatial Mismatch
Strengthen career pathways
Create housing near jobs and transit
Improve access to public transit
Emphasize equity in data collection and public engagement
Notes: Key Message: Addressing spatial mismatch ensures that low-income workers are matched with jobs that provide gainful employment, providing opportunities for economic advancement.
Talking Points:
Strengthen career pathways
  Provide training and opportunities for career advancement
Create housing near jobs and transit
  Increase affordable housing near jobs and transit
Improve access to public transit
  Reduce or eliminate transit fares
  Provide direct access between residential areas and employment centers (e.g. transit circulator)
Emphasize equity in data collection and public engagement
  Focus on identifying and addressing the specific needs of underserved communities
References:
Stacy, C. et al. (2019). Too far from jobs: spatial mismatch and hourly workers. https://www.urban.org/features/too-far-jobs-spatial-mismatch-and-hourly-workers
Stacy, C. et al. (2020). The unequal commute. https://www.urban.org/features/unequal-commute

## Slide 22: Transit Justice

## Slide 23: Transit Justice Principles
Equitable
Sustainable
Economically productive
Affordable
-National Campaign for Transit Justice
Notes: Key message: Transit investment must remove barriers for minority groups, low-income populations, and people with disabilities
Talking points:
Transit justice principles are as follows:
Equitable: A car-based transportation system created barriers to mobility that reinforced social inequities.
Sustainable: Investments must expand access to bus and train service to avert single use vehicles
Economically productive: Expand workers access to jobs, employer access to the workforce, customer access to business, and business access to customers
Affordable: Access to transit should not be contingent on one’s ability to pay, investments should establish programs to provide fare relief
Transportation should ensures personal freedom, access, and connection
  Freedom: well-designed and maintained transportation system that allows people to go where they want easily and safely
  Access: safe, healthy, reliable, and affordable transportation that supports access to jobs, education, culture, and recreation
  Connection: transportation options that make it easier to get from one place to another
  -Portland Bureau of Transportation
References:
City of Portland, Oregon. (n.d.) strategic plan overview. https://www.portlandoregon.gov/transportation/article/741201
National Campaign for Transit Justice. (n.d.). Transit justice principles. https://transitjustice.org/about/transit-justice-principles/

## Slide 24: Transit Accessibility Measures
First/last-mile access
  Walking, cycling, other
Transit service
  Location, intensity, frequency of service, hours of evaluation
Commute time
  Reduction in travel time
Location of transit stops and routes in relation to underserved communities
Access to employment, community services, education, and other essential destinations
Notes: Key Message: This list is a sampling of a several accessibility measures.
Talking Points:
Ultimately, transit that meets the needs of system users with safe, affordable, reliable, convenient transportation options to meet daily needs
References:
Williams, K. et al. (2020). Transportation equity scorecard – A tool for project screening and prioritization. https://www.cutr.usf.edu/wp-content/uploads/2021/09/The-Transportation-Equity-Scorecard-User-Guide.pdf

## Slide 25: Chicago Case Example
Source: Klumpenhouwer, W., Allen, J., Li, L., Liu, R., Robinson, M., Da Silva, D. L., Farber, S., Karner, A., Rowangould, D., Shalaby, A., Buchanan, M., & Higashide, S. (2021). A Comprehensive Transit Accessibility and Equity Dashboard.Findings, July.
Affordable transit access for equity neighborhoods to low-wage jobs during weekdays from 7am-9am.
Notes: Key Message: The maps developed by the Transit Center show the extent to which residents have equitable access to jobs, shopping, healthcare, and other essential destinations using transit.
Talking points:
The map can be adjusted for the following variables:
Destinations (jobs, low wage jobs, parks, grocery stores, hospitals, etc.)
Time period
Time available to travel
Region (metropolitan statistical area, economic region, urban core, and equity neighborhoods),
Trip affordability
Demographic groups
Equity neighborhoods are defined as “areas that local transit advocates and TransitCenter identified as meriting additional resources for transit improvements because of past disinvestments or marginalization in planning decisions.”
In Chicago, the analysis showed the following:
Less access to opportunity for minority communities
Transportation and land use patterns limit accessibility
Transit costs reduce opportunities to access essential destinations
References:
Klumpenhouwer, W., Allen, J., Li, L., Liu, R., Robinson, M., Da Silva, D. L., Farber, S., Karner, A., Rowangould, D., Shalaby, A., Buchanan, M., & Higashide, S. (2021). A Comprehensive Transit Accessibility and Equity Dashboard.Findings, July.

## Slide 26: Gentrification and Displacement

## Slide 27: Transit-Induced Gentrification
Investments in transportation improve accessibility
Communities are renovated and redeveloped
Property values increase
Lower-income community members are priced out
Transit-oriented development has the potential to benefit everyone, but it must account for the needs of the working class and economically marginalized.
Notes: Key message: Transit-induced gentrification is a socioeconomic byproduct of transit-oriented development
Talking Points:
Transit-induced gentrification is typically observed in the following phases:
Accessibility is improved through transportation
Low-income communities experience an influx of middle class or wealthy people
Homes and businesses are renovated
Often results in an increase in property values and the displacement of lower-income residents
Gentrification indicators are most effective when identified by local agencies and communities, but should consider the needs of renters vs homeowners and those dependent on transit
References:
Turrentine, J. (2018). When public transportation leads to gentrification. https://www.nrdc.org/onearth/when-public-transportation-leads-gentrification
Auger, D. (2007). The politics of revitalization in gentrifying neighborhoods: The case of Boston’s South End. https://www.tandfonline.com/doi/abs/10.1080/01944367908976999

## Slide 28: Types of Displacement
Source: https://www.nctcog.org/nctcg/media/Transportation/DocsMaps/Plan/GentrificationStudy.pdf
Notes: Key Message: “The most vulnerable to displacement are minorities, seniors, those with disabilities, and other economically disadvantaged groups” (NCTCOG, 2019)
Talking Points:
There are various types of displacement, but they most severely affect the most vulnerable population groups.
References:
NCTCOG. Transportation and gentrification: A toolbox for positive neighborhood change. https://www.nctcog.org/nctcg/media/Transportation/DocsMaps/Plan/GentrificationStudy.pdf

## Slide 29: Affordability Example: Displacement Risk
Southern California Association of Governments (SCAG)
Conducted risk analysis for gentrification and displacement
Source: SCAG, 2020
Notes: Talking Points:
Another consideration for affordability is displacement risk
  The Southern California Association of Governments (SCAG) in the 2012-2035 regional transportation plan conducted an analysis of risk of gentrification and displacement, based upon areas with a high proportion of people at risk of displacement.
  This metric measured: percent of minority population, poverty rate, share of 65+ population, percent of households without a car, percent of non-English speaking, population without a high school diploma, and percent of renters.
  The SCAG methodology looked at gentrification in Transit Oriented Communities (TOCs), which are defined as neighborhoods within ½-mile distance of existing rail stations, compared to the greater region and High Quality Transit Areas (HQTAs). According to the analysis, Hispanics and seniors have seen less growth in TOCs during the 2000-2013 period while median gross rent has increased and median gross income has decreased in these TOCs compared to the greater region. SCAG recognizes these different growth patterns of possible evidence of gentrification and displacement – but acknowledges the limits of their statistical testing and the need for continued monitoring.
  The 2020–2045 Regional Transportation Plan/Sustainable Communities Strategy expanded the “Gentrification and Displacement” analysis to non-transit areas; It considers race, educational attainment, rent vs. homeowners as indicators to determine communities vulnerable to gentrification and displacement
  The SCAG Regional Target Advisory Committee (RTAC) recommended that displacement and gentrification, as a result of changing land uses and increased housing costs, should be addressed and specifically avoided to the extent possible in the SCS
References:
Southern California Association of Governments. (2020). Plan performance: Environmental justice. https://scag.ca.gov/sites/main/files/file-attachments/0903fconnectsocal_environmental-justice.pdf?1606001617

## Slide 30: California Case Example
San Diego, Los Angeles, Sacramento, San Francisco
New multifamily buildings constructed
Many households in the neighborhoods could not afford to rent a unit in these buildings
Source: https://www.urbandisplacement.org/maps/los-angeles-gentrification-and-displacement/
Notes: Key Message: An article by the San Diego Tribune reported that housing built around transit resulted in displacement of residents most dependent on transit services
Talking Points:
In San Diego, Los Angeles, Sacramento, San Francisco housing costs increase near rail and other forms of transit
Nearly 400 new multifamily buildings were constructed within half a mile of a transit stop over 5 years
  The average monthly rent for a two-bedroom apartment was more than $3,500.
Many households in the neighborhoods could not afford to rent a unit in these buildings
  Median household income averaged less than $64,000.
References:
Smith, J. (2018). Efforts to build housing around transit threaten to price out those most dependent on bus and rail. https://www.sandiegouniontribune.com/news/environment/sd-me-transit-gentrification-20180517-story.html
Turrentine, J. (2018). When public transportation leads to gentrification. https://www.nrdc.org/onearth/when-public-transportation-leads-gentrification

## Slide 31: How to Mitigate Gentrification and Displacement
Create and maintain affordable housing. Examples include:
  Inclusionary zoning
  Housing trust funds
  By-right zoning
  Property tax strategies
  Renter protection
  Preserving subsidized housing
Empower the community. Examples include:
  Create a community benefit agreement
  Implement community land trusts
  Develop and implement neighborhood plans
Notes: Key Message: There are a multitude of strategies that can be implemented to address gentrification and displacement.
Suggestion:
Before you move to the next slide, complete the knowledge probe activity Module 6 Probe Question #5 (see the module outline for more information):
Ask students to discuss the strategies provided on the slide.
What other strategies can be used to address the need for transit while also mitigating the potential gentrification and displacement of low-income community members?
References:
NCTCOG. Transportation and gentrification: A toolbox for positive neighborhood change. https://www.nctcog.org/nctcg/media/Transportation/DocsMaps/Plan/GentrificationStudy.pdf

## Slide 32: Broadband and the Digital Divide

## Slide 33: Digital Divide
Limited or no internet access and are less likely to own certain digital devices
  Low-income households
  Older people in poverty
  Black and Hispanic adults
  Persons with disabilities
There are locational disparities in internet access between urban, suburban, and rural areas
https://www.pewresearch.org/fact-tank/2021/06/22/digital-divide-persists-even-as-americans-with-lower-incomes-make-gains-in-tech-adoption/
Notes: Key Message: There is a gap between people who have access to digital devices and the internet and those who do not.
Talking Points:
Roughly a quarter of adults with household incomes below $30,000 don’t own a smartphone
  43% of adults with lower incomes do not have home broadband services
  41% do not have a desktop of laptop computer
Black and Hispanic adults are less likely than white adults to own a traditional computer or have high-speed internet at home, although, ownership trends for devices such as smartphones and tablets are similar between each racial group.
Broadband – high-quality high-speed internet service
References:
Vogels, E. (2021). Digital divide persists even as Americans with lower incomes make gains in tech adoption. https://www.pewresearch.org/fact-tank/2021/06/22/digital-divide-persists-even-as-americans-with-lower-incomes-make-gains-in-tech-adoption/
Atske, S. and Perrin, A. (2021). Home broadband adoption, computer ownership vary by race, ethnicity in the U.S.. https://www.pewresearch.org/fact-tank/2021/07/16/home-broadband-adoption-computer-ownership-vary-by-race-ethnicity-in-the-u-s/
Perrin, A., and Atske, S. (2021). Americans with disabilities less likely than those without to own some digital devices. https://www.pewresearch.org/fact-tank/2021/09/10/americans-with-disabilities-less-likely-than-those-without-to-own-some-digital-devices/
Vogels, E. (2021). Some digital divides persist between rural, urban and suburban America. https://www.pewresearch.org/fact-tank/2021/08/19/some-digital-divides-persist-between-rural-urban-and-suburban-america/
Swenson, K. and Ghertner, R. (2020). People in low-income households have less access to internet services. https://aspe.hhs.gov/sites/default/files/private/pdf/263601/Internet_Access_Among_Low_Income.pdf

## Slide 34: Digital Divide and Transportation Equity
Transportation technology is rapidly advancing
Applications for real-time public transit information
Contactless smart cards
Persons without a smart phone, credit card, and/or no internet access have little to no access to these services
Rideshare, e.g., Uber and Lyft
Automated fare collection systems
Notes: Key Message: Due to the digital divide, many persons in underserved communities do not have access to critical technology needed to increase access to opportunity
Talking Points:
Broadband provides an avenue for access to education, employment, socialization, health (telemedicine, etc.) and many other resources. Those who do not have access to broadband cannot benefit from these services.
References:
Stephens, J. (2015). Digital divide includes transportation and tech. https://www.planetizen.com/node/73640
Schmitt, A. (2015). 10 cities that are getting “wired transportation” right. https://usa.streetsblog.org/2015/02/04/10-cities-that-are-getting-wired-transportation-right/

## Slide 35: San Diego Case Example
Affordability was identified as a major concern for those without internet at home
More low-income households, older adults, and minority populations do not have internet access or a computer
Source: https://storymaps.arcgis.com/stories/f204b9b88ea4483b8a0d46c8d099c3a7
Notes: Key Message: The San Diego Association of Governments (SANDAG) evaluated broadband access, adoption, and infrastructure in the San Diego Region.
Talking Points:
Communities with limited to no access to broadband were most affected by COVID-19 and related increases in unemployment
References:
SANDAG. (n.d.) The digital divide in the San Diego region. https://storymaps.arcgis.com/stories/f204b9b88ea4483b8a0d46c8d099c3a7

## Slide 36: San Diego Case Example
Strategies developed to address the digital divide
Source: https://storymaps.arcgis.com/stories/f204b9b88ea4483b8a0d46c8d099c3a7
Notes: Key Message: The San Diego Association of Governments (SANDAG) has developed a regional digital equity strategy to address the digital divide in the region
References:
SANDAG. (n.d.) The digital divide in the San Diego region. https://storymaps.arcgis.com/stories/f204b9b88ea4483b8a0d46c8d099c3a7
SANDAG. (2021). Regional digital divide equity strategy and action plan. https://www.sandag.org/index.asp?classid=13&projectid=614&fuseaction=projects.detail

## Slide 37: Additional Strategies to Mitigate the Digital Divide
Provide the necessary infrastructure to expand broadband service
Offset the cost of broadband, particularly for low-income households
Provide public access to the internet
Educate the public to improve digital literacy
Create accessibility apps for persons with disabilities
Source: Iliescu Victor from Pexels
Notes: Key Message: Broadband is essential for increasing access to opportunity.
Suggestion:
Before you move to the next slide, complete the knowledge probe activity Module 6 Probe Question #6 (see the module outline for more information):
Ask students to discuss the strategies provided on the slide.
What other strategies can be used to provide access to broadband? How do they improve accessibility needs for underserved populations?
References:
Tomer, A., Fishbane, L., Siefer, A., and Callahan, B. (2020). Digital prosperity: How broadband can deliver health and equity to all communities. https://www.brookings.edu/wp-content/uploads/2020/02/20200227_BrookingsMetro_Digital-Prosperity-Report-final.pdf
USDOT. (2016). How we grow opportunity for all. https://www.transportation.gov/smartcity/how-we-grow-opportunity

## Slide 38
How can we improve access to opportunity for underserved populations?
What are the potential consequences of the strategies identified?
Are there any mitigating measures that can improve anticipated outcomes for underserved populations?
Notes: Suggestion:
Before you wrap up the lecture, complete the knowledge probe activity Module 6 Probe Question #7 (see the module outline for more information):
Encourage students to think about the issues for access to opportunities identified throughout the lecture. Ask them to recall the strategies they identified and discussed during the probe questions and subsequent discussions.
What other strategies can be used to improve access to opportunity for underserved populations? How do these strategies improve opportunities for social and economic mobility? What are the potential consequences of the strategies identified? Are there any mitigating measures that can improve anticipated outcomes for underserved populations?