## Slide 1: Computer Networks
Chapter 15
Notes: This PowerPoint should be used with the “Computer Networks” chapter of the Fundamentals of Information Technology textbook.
Written for the Florida Public School System DIGITAL INFORMATION TECHNOLOGY (8207310

## Slide 2: Topics
Introduction to Computer Networks
The Internet
Technology as a Stack
Computer Network Security

## Slide 3: Introduction to Computer Networks
Computer networks can be defined as the interconnection of information systems through the use of components designed to communicate using standardized technologies.
  Computers interact with networks through the use of specialized hardware components designed to communicate data in a very consistent way.
  Since the invention of the telegraph, communication technologies have evolved considerably and eventually motivated the standardization of network architecture.

## Slide 4: The Internet
The Internet can be defined as an interconnection of individual computers across the world through an interconnection of networks using a standardized set of communication protocols.
  The Internet allows people and systems to communicate in a consistent way as data moves across the multiple networks which are interconnected across the globe.
  When we think of the Internet, it’s easy to relate it to what we know about the world wide web.
  The world wide web is what people use every day to do things like shop online or ask “Siri” a question, or post videos to social media platforms such as Instagram.

## Slide 5: Technology as a Stack

## Slide 6: Technology as a Stack
As Internet technologies were standardized, they were eventually constructed as a stacked layer of technologies, specified as the Open Standards Interconnection (OSI) Model.
Today, the OSI Model has been simplified using a core set of standardized technologies which are described as the TCP/IP stack.
The TCP/IP stack is a five-layered network architecture.

## Slide 7: TCP/IP Stack
Below is a summary of the TCP/IP stack layers and their described functional networking tasks.
Layer Number | Layer Name | Networking Task
5 | Application | Specify the needs of users
4 | Transport | Organize data for network transmission
3 | Network | Identify and locate the destination network
2 | Data Link | Remove errors during transmission and label devices
1 | Physical | Signals transmitted across a wire

## Slide 8: Physical Layer
The Physical layer of the TCP/IP stack transmits information over a distance and requires technology that can transmit signals across a physical medium.
  Different types of media include copper wire, optical fiber, or various forms of wireless communication.
  The signals are generated by capturing energy from an energy source and encoding the data using this energy for transmission over the physical medium.

## Slide 9: Physical Layer
Depending on the physical medium, signals are commonly transmitted as digital or analog.
A digital signal is typically generated when an energy source transmitting the signal turns on and off.
If the energy is present, we can measure the data as a 1.
If the energy is absent, we can measure the data as a 0.
This continuous signal changes in amplitude and frequency forming a sine wave as energy varies in intensity and time.

## Slide 10: Physical Layer
The 1s and 0s data generated by signals traveling through a physical medium is commonly referred to as binary data.
Binary data captured from signals can be encoded to represent characters humans can understand.
For instance, the American Standard Code for Information Interexchange (ASCII) includes numerical representations (decimals) which can be used to convert letters in the English language to binary data.

## Slide 11: Physical Layer
The table below describes how the word “hello” can be represented as a binary number using the ASCII code.
Character | ASCII Decimal | Binary
h | 104 | 01101000
e | 101 | 01100101
l | 108 | 01101100
l | 108 | 01101100
o | 111 | 01101111

## Slide 12: Physical Layer
Early physical media used in networks were made of copper wiring.
The most common type of network copper cable used today is called Cat5e and it has a connector on its end called RJ45.
Cat5e network cable with connector end RJ45

## Slide 13: Physical Layer
Another common physical medium used in networks is optical fiber.
Optical fiber is typically bundled inside of fiber optic cable.
Optical fiber inside a fiber optic cable

## Slide 14: Data Link Layer
The Data Link layer functions to provide both addressing and error detection.
  Imagine a scenario where you are using your laptop at home to complete a homework assignment and then you need to submit online.
  You would want your homework to find its way through the Internet to its final destination.
  Additionally, you would also want your homework to arrive at its destination in the exact state as you completed it with no errors.
  This is where the Data Link layer is necessary.

## Slide 15: Data Link Layer
The physical address plays an important role in making sure that your homework finds its way toward the final destination.
In the example output you can see that the Microsoft Windows operating system has identified that the active interface connection with the physical address of 6D-B1-00-5U-03-9R.
The Data Link layer is implemented within the interface where the physical address can be used to uniquely identify a device connected to a network.
Example: if you own a laptop with Microsoft Windows installed you can run a command within a command prompt which will output the MAC address actively being used: C:\Users\clinton> ipconfig /all
  Wireless LAN adapter Wi-Fi:
  Description . . . . . . . . . . . . : Intel® Wi-Fi AX200 160Hz
  Physical Address. . . . . . . . . : 6D-B1-00-5U-03-9R
  DHCP Enabled. . . . . . . . . . . : Yes
  IPv4 Address . . . . . . . . . . . : 192.168.1.26

## Slide 16: Data Link Layer
The Data Link layer not only functions to provide addressing, it also serves the function of error detection.
  There must be a technology within a layer of the TCP/IP stack which can detect if any errors were introduced during the transmission of a signal.
  Errors can occur when a signal is disrupted by events such as power outages or power spikes.
  When events like this occur, there must be a technology capable of detecting errors to improve the reliability of the network.

## Slide 17: Data Link Layer
Errors are typically detected on a network using specialized algorithms.
This is where mathematicians really get to use their skills.
The algorithm used by networks to detect errors is known as a Cyclic Redundancy Check (CRC).
Recall that an algorithm is a set of steps used to accomplish a desired output.
The algorithm is designed to detect an error in the transmitted data.

## Slide 18: Network Layer
The Network layer function is to transfer packets of data from a source computer, such as a laptop on your home network, to a destination computer through one or more networks
  This task is also called Routing and is performed by networking devices called Routers.
  You may have a router in your home that was supplied by your internet service provider that allows you to connect your home devices to resources across the global Internet.

## Slide 19: Network Layer
The Network layer functions to transfer packets across multiple networks.
A packet of data is a small segment of a larger piece of data sent over a network.
Communicating signals and data over networks involves the use of standard protocols.

## Slide 20: Network Layer
The most common protocol used at the Network layer is the Internet Protocol (IP).
IP plays an essential role in the Network layer and is the standard responsible for routing packets across interconnected networks.
IP is managed on networks by professionals who configure routers and facilitate routing by assigning IP addresses to devices.
An IP address is a unique identifier that has been assigned automatically or manually to devices accessing a network.
IP address is automatically or manually assigned by technology designed to manage devices connecting to a local network or the Internet.

## Slide 21: Transport Layer
The Transport layer functions to ensure that data is reliably delivered to its destination over a network.
  The Transport layer includes technology designed to track data as it is broken down into small segments.
  Segmentation is the process of breaking data down into smaller units to allow for a more compact transmission over a network using IP.
  This is useful because IP has a limitation on the size of packets it can transfer over a network.
  Once a receiving technology receives all of the segmented data, the Transport layer is then responsible for reassembling these segmented packets of data back into their original form so that they can be used by an application such as a web browser.

## Slide 22: Application Layer
The Application layer functions to support the needs of technology users. With the support of the Application layer, the technology industry has invented many functional uses for the Internet to fit our daily lives.
The table below summarizes five common application protocols which have been developed to support a variety of applications.
Application Protocol | Functional Description
HTTP (Hyper Text Transfer Protocol) | Used in the world wide web to communication data from web pages
SMTP (Simple Mail Transfer Protocol) | Used to send and receive email
FTP (File Transfer Protocol) | Used to communicate and transfer files between computers
SSH (Secure Shell) | Used to send commands between computers
IM (Instant Messaging) | Used to exchange text-based messages using computers or mobile devices

## Slide 23: Network Support Services: DHCP
The Dynamic Host Configuration Protocol (DHCP) service was developed to manage the assignment of IP addresses on a network.
  If a network allows you to connect to it, a DHCP service assigns your device an IP address on the network.
  This assigned IP address is then used by your device so that you can operate applications capable of communicating on the Internet.

## Slide 24: Network Support Services: DNS
Domain Name Service (DNS) is another common service used on computer networks.
  This service is used by the Domain Name System which includes a set of databases responsible for translating IP addresses into domain names.
  To see DNS in action, you can execute a WHOIS query.

## Slide 25: Network Support Services: DNS
Result of WHOIS query on https://www.usf.edu/

## Slide 26: Computer Network Security

## Slide 27: Computer Network Security
Networks were originally motivated and designed around the concept of communication through technology.
These technologies were not designed to consider the risks of intentional harm to the systems or data as a result of a cyber-attack.
A cyber-attack is an attempt by a malicious person or program to damage or destroy a computer network and the systems that support it.
Protecting networks using security technology is a necessity in today’s world.

## Slide 28: Computer Network Security
One specific and important security technology that is designed to protect networks is a firewall.
A firewall is a computer that is positioned on the network between the devices used inside a network and the outside world.
The firewall computer keeps a careful eye on all the incoming network traffic and applies filters that can block any unwanted or malicious packets.
The filters are configured by IT professionals who can assign a set of rules that are designed to identify known harmful network traffic.
Firewalls keep us all safe when we use our devices to communicate on the Internet.

## Slide 29: Computer Network Security
Communicating on a network securely typically involves the use of encryption technologies.
Put simply, encryption is the process where you use an algorithm to scramble data into a secret encoded message that can only be unlocked with a unique and guarded key.
One such type of encryption uses a digital certificate.
You can use these digital certificates to encrypt data being transmitted over a network such as an email, text, or instant message.
It is important to use strong algorithms that are so complex that it would be impractical for anyone to decrypt.

## Slide 30: The end